## Slide 1: Presentation-I
Literature Review and Proposed Idea on collision validation

## Slide 2: Papers Covered For Topics
Numerical simulation of head-on collision of two coaxial vortex rings –Cheng,Lou and Lim
  General Idea of co-axial vortex collision for identical and different vortices and azimuthal instability.
Head-on collision of two vortex rings - Oshima(1978)
  Experimental Study of based smoke vortex ring collisions.
Head-on collision of viscous vortex rings – Stanway, Shariff, Hussain
  Research on temporal changes in KE and ensthrophy and the iterative solution to the problem.
A brief introduction to vortex dynamics and turbulence - Mofftat
Head-on collision of two co-axial vortex rings - Chu, Wang, Chang, Chang and Chang

## Slide 3: Review
Vortex Rings are vortices produced by turbulence from an external source.
As a single entity, the body shows similar behaviour in ideal(inviscid) and viscous flow.
However, interactions with other vortex rings and other solid bodies show deviations.
The vortex rings in general can be described by the governing equation
div(u)=0
The vorticity Ω and the velocity u, decrease and increase according to the gaussian function which is dependent on core radius and circulation.
As two (opposite circulation) vortex rings approach each other, they cause mutual induction as a result of which axial velocity decreases but radial velocity increases.
In case of identical vortex rings,the velocity rediction and the radial expansion are similar to both.

## Slide 4: Review(Contd.)
In case of CR > 1 or CR < 1, the core radii will be different leading to different rates of velocity reduction and expansion rates.
In this case, in close proximity, the induced velocity of thicker ring will be more than that of the thinner ring and will cause easy slip-over of thicker ring on thinner ring.
With increase in CR, there is a decrease in KE and vorticity dissipation but increases ensthrophy.
Increase in Re causes increase in vorticity intensity and ensthrophy.
If the ring release velocity is very high and the Re is also along the higher line, the ring develops a wavy nature.
When 2 vortex rings of this type interact there is a formation of vortex ringlet and loops.
Depending on the value of CR, the ringlets form have different angles from the plane of collision.
The temporal trends in KE, Ensthrophy are same as before.

## Slide 5: Proposition
Determining the effect of vorticity and azimuthal wave number on ringlet size and angle of deviation
Implementation Methodology
Changing exit velocity through orifice to change wave number and evaluate changes in ringlet dimension.
We know, higher CR means a higher angle of deviation from the plane of collision.We can fix CR and modulate the circulation values to bring changes.

## Slide 6: Presentation - II
Vortex Ring Formations

## Slide 7: Papers Covered
VORTEX RINGS - EXPERIMENTS AND NUMERICAL SIMULATIONS -Damian , Talasce, Simonesque Mihailescue
      Analysing a single vortex ring after formation.
Circulation Generation- Rosenfield
      Process of creating vortex rings from circular nozzles
Vortex Ring Time Scale – Karim, Rambod and Shariff

## Slide 8: Ansys Simulations Update
Have tried analysing transient fluid flow through a nozzle alone.
Yet to setup the container system for the nozzle in 3D to make the formation of vortex.
Learning UDF for making variable input parameters for changing vortex size and circulation.

## Slide 9: Single Nozzle Flow(Trial)

## Slide 10: Presentation-III
Formation of vortex rings and starting collisions

## Slide 11: Papers Reviews (Vortex Formation)
The Ring Vortex: Concepts for a Novel Complex Flow Phantom for Medical Imaging – Ferrari, Ambrogio, Walker and more
  Governing Equations on Vortex Ring
  Method For creating Vortex Rings in ANSYS
  Velocity UDF set up
Numerical Simulations of 3D Compressible Vortex Ring– Dora and more
  General Dimensions of apparatus
  Difference between density dependent and independent vortex rings
Circulation Generation and Vortex Ring Formation by Conic Nozzles – Rosenfield, Katija, and Dabiri
  ANSYS Setup for Vortex ring formation
  Dependence of nozzle length and exit diameter on ring characteristics.

## Slide 12: Papers Reviews (Vortex Formation)
Direct numerical simulation of a laminar vortex ring – James, Madnia
  Numerical Techniques on the formation of vortex rings
  Whether to choose nozzle or orifice.
Simulations of the formation of an axisymmetric vortex ring– Heeg and Riley
  General Dimensions of apparatus
  Difference between density dependent and independent vortex rings
Vortex Dynamics – PG Saffman
  General Equations of Vortices
  Relation between modulating terms and ring characteristics

## Slide 13: Review
Formation of vortex rings is directly possible through orifices and nozzles.
Vortex rings are analytically classified into 3 types – Hill, Thick and Thin
In case of nozzles the following points must be kept in mind :
Two sections:
  A straight tube of length Ls= 40 cm and a constant diameter of Dp=2.5 cm
  A conic nozzle of length Ln=5.1 cm dimensions are chosen to match the experimental setup and exit diameter De of De /Dp=0.2, 0.4, 0.6, 0.8, or 1. The computational domain downstream of the nozzle exit has a length of L/Dp=32, and the outer boundary is at a radial distance of H/Dp=4.
  An orifice is a limiting case of a nozzle when De /Dp=1 and L=0
The circulation of a vortex ring is directly dependent on the De/Dp
ratio.
On the similar lines, for a given circulation and impulse, the kinetic energy is inversely dependent on the diameter ratio as mentioned above.
Decreasing the length increases the 2-dimensional component of the ring, thus increasing circulation.

## Slide 14: Comparison

## Slide 15: Design Used

## Slide 16: Model

## Slide 17: UDF Used

## Slide 18: Modified UDF for Explicit Slug Formation
This UDF considers an exponential decrease in the initial velocity amplitude at the starting point.

## Slide 19: Current Simulations
X - Velocity
Y - Velocity

## Slide 20: Current Simulations

## Slide 22: Collission Papers Covered
Numerical simulation of head-on collision of two coaxial vortex rings – Cheng, Lou
Head-on Collision of laminar vortex rings – Stanway Shariff

## Slide 23: External Points Seen
Optimum density fluids have to used for easier visualization of the collision and for maintaining the strength of the ring.
Collision should take place at points further away from the exit, especially in case of an orifice.
Identical coaxial rings will be formed by same exit diameter and length.
Coaxial rings with different core radii can be formed by changing between orifice and nozzle. However, length should be kept constant to account for the same 2-dimensional component.

## Slide 24: Collision Update

## Slide 25: Presentation- IV
Vortex ring collision validation

## Slide 26: Clarity of Ring

## Slide 27: Clarity and Stability

## Slide 28: Oshima Trials

## Slide 29: Validation (Net Velocity Distribution with radius)
Chart: Velocity Ratio vs Radius
| -9.6000000799999999E-2 | -7.4666663999999994E-2 | -5.3333330900000003E-2 | -3.1999997799999999E-2 | -1.06666647E-2 | 1.0666668400000001E-2 | 3.20000015E-2 | 5.3333334599999997E-2 | 7.4666663999999994E-2 | 9.6000000799999999E-2
Velocity Ratio | 0 | 0.2735 | 0.22435 | 0.5676 | 0.77338 | 0.78191 | 0.58205 | 0.22702 | 0.26777 | 0.033373

## Slide 31: Collission (Papers Covered)
Interaction of Two Vortex Rings moving Along common axis of symmetry – Oshima, Kambe, Asaka
  Numerical Approach to collision
  Provided slug model for the collision process
  In this experiment, 1 D collision was created between 2 rings moving in same direction.
Numerical Simulations of Two Coaxial Vortex Rings Head-on Collision – Guan , Wei and more

## Slide 32: System Used

## Slide 33: Measurement Points

## Slide 34: Vorticity Plots

## Slide 36: Simulations Based on Cheng Papers

## Slide 37: Presentation V
Moving Planes and MATLAB

## Slide 38: Dynamic Contours
Set up an expression to move the plane to the position of the maximum vorticity.
True value of radius can be measured by this.
Set up a point at Maximum Vorticity, Probed coordinates at that point to set up the plane and then moved the plane along the X direction.

## Slide 40: Plotting Radius
Files at 15 timesteps were taken and exported to MATLAB.

## Slide 43: Circulation Ratios
Polyline was created at average points of the ring.
Line integral of tangential velocity was taken along the polyline.
Plot was made directly in CFD-Post as polyline couldn’t be exported to MATLAB.

## Slide 46: LIM NICKELS MODEL

## Slide 47: Presentation - VI
Instability Model, Looping and Slow Trials

## Slide 48: Instability Trials

## Slide 49: Azimuthal Instability
Happens at higher Reynolds number
Current analysis performed at 2000 Reynolds number.
Apparatus same as earlier.
The only exception is that the speed was increased tremendously to 15 m/s to provide N = 15.

## Slide 51: Radius Growth in Instability Case

## Slide 52
Diameter vs Time
(High Velocity)
Diameter vs Time
(Low Velocity)

## Slide 53: Visualisation
Isosurfaces were made Average + 20% Std. Deviation in order to maintain visibility.
As soon as collision started, the sine wave perturbation was seen and the looping mentioned was observed.

## Slide 55: Perturbation based linking
Local Looping for shorter ring formation

## Slide 56: Secondary Collissions

## Slide 57
There is a secondary collision which occurs slightly concentric regions of high vorticity to the major collision.